DIY基于摄像头的激光测距仪

作者：Rockets   文章来源：www.RoboticFan.com   更新时间：2008-5-11 22:10:33  打印此文    浏览数： 5097

### 前言

本文是由RoboticFan网友Rockets翻译的一篇由国外机器人爱好者撰写的激光测距仪的文章。小编认为这篇文章具有相当的实用型和可操作性，发散一下思维能力，可以发现有很多应用。

### 介绍

有很多现成的测距组件包括超声波、红外线、甚至是激光测距仪。这些设备运行的很好，但是对于飞行机器人来说，重量是一个主要考虑因素。一个可行的办法是增加现有组件的功能，并安装在机身上。例如微型空中机器人的有效载荷是100g。它能利用USB连接的摄像头（或mini无线摄像头）执行视觉任务，例如避障等。更好的是，如采用两个摄像头，能提供立体的机器视觉，这样能增强避障性能，因为双镜头提供了视觉深度。但缺点是需要增加另外一个摄像头的重量。这篇文章就是讨论如何利用一个激光笔和一个摄像头来提供一个单镜头机器视觉和测距的。

这个项目很大一部分是基于下面这个教程的
http://www.eng.buffalo.edu/ubr/ff03laser.php

### 工作原理

下图显示了如何将激光点投射到目标物上，并在摄像头上显示。摄像头和激光点的距离是可以通过计算而得出的。公式很简单，因此这个技术在需要很快运行的机器视觉应用上是适合的。

介绍一下工作原理。一束激光被投射到目标物上，并在摄像头上被显示。激光束被认为是理想的平行于摄像头的中心光轴。激光点由摄像头的其余部分所捕获。一个简单的计算就是寻找最亮点。如果设激光点就是这个场景的最亮点（似乎在室内我的激光发射器确实是最亮的），那么这个点的位置在图帧中的位置是确定的。然后我们只需要计算这个点在沿着y轴的距离，就能计算出目标物离摄像头的距离，激光点距离中心越近，离目标物越远。

如同公式所示，距离D是可以被计算出来的。

为了计算这个等式，我们需要知道激光器和摄像头之间的距离h，这是个常数，还有角度，角度可以计算。

其中：

pfc＝从焦平面到中心的像素数量
rpc＝单个像素的弧度
ro＝弧度补偿（弥补对齐错误）


代入上式，我们得到：

这样，从图像中就能将焦平面到激光点像素数计算出来。那其他的常数怎么办呢？我们需要执行一个校准来得到这些数据。

为了校准这个系统，我们需要收集一系列测量的数据，每次测得的目标物的距离和这个激光点离中心点的像素数。数据如下

| 校正数据 |
| --- |
| pixels from center | actual D (cm) |
| 103 | 29 |
| 81 | 45 |
| 65 | 58 |
| 55 | 71 |
| 49 | 90 |
| 45 | 109 |
| 41 | 127 |
| 39 | 159 |
| 37 | 189 |
| 35 | 218 |

使用下面的公式，我们能够利用激光器和摄像头之间的距离h和真实距离计算出真实的角度：

θactual＝真实角度
Dactual＝真实距离（测量得出）

现在我们有了公式中的每个数值，我们可以利用一个关系式来计算点离中点的像素数。我用了一个线性关系式。这个公式看起来很有用，…… 
从我的校正数据中，我计算出: 
Offset (ro) = -0.056514344 radians 
Gain (rpc) = 0.0024259348 radians/pixel 
使用:

下表是列举了根据上面ro和rpc值计算出的距离值，实际距离值和误差： RoboticFan

| 实际和计算的测量数据 |
| --- |
| pixels from center | calc D (cm) | actual D (cm) | % error |
| 103 | 29.84 | 29 | 2.88 |
| 81 | 41.46 | 45 | -7.87 |
| 65 | 57.55 | 58 | -0.78 |
| 55 | 75.81 | 71 | 6.77 |
| 49 | 93.57 | 90 | 3.96 |
| 45 | 110.85 | 109 | 1.70 |
| 41 | 135.94 | 127 | 7.04 |
| 39 | 153.27 | 159 | -3.60 |
| 37 | 175.66 | 189 | -7.06 |
| 35 | 205.70 | 218 | -5.64 |

### 所需零部件

我的测距仪没有多少部件。我使用一块硬纸板来固定激光发射器和摄像头。摄像头和激光发射器被平行的布置在一起。

我组装的测距仪是这样的

### 软件

我通过两个方式编写了这个软件，一个是vc++，一个是VB。你能发现VB版本的软件会比VC＋＋的软件更容易一些，但是各有取舍。VC++版本能够自由的加入其他软件中？VB版本需要第三方软件支持（在Visual Studio中）

### Visual Basic

vb_laser_ranger.zip

这里可以下载到我的VB版本软件。
要使用上面的程序，你必须要安装VideoOCX ActiveX 控件

主程序如下：

Private Sub exit_Click()
    ' only if running...
    If (Timer1.Enabled) Then
        
        Timer1.Enabled = False  'Stop Timer
        VideoOCX.Stop
        VideoOCX.Close
                
    End If
    
    End
End Sub

Private Sub Start_Click() 'Init VideoOCX Control, allocate memory and start grabbing
         
    If (Not Timer1.Enabled) Then
        Start.Caption = "Stop"
  
        ' Disable internal error messages in VideoOCX
        VideoOCX.SetErrorMessages False
    
        ' Init control
        If (Not VideoOCX.Init) Then
            ' Init failed. Display error message and end sub
            MsgBox VideoOCX.GetLastErrorString, vbOKOnly, "VideoOCX Error"
            End
        Else
            ' Allocate memory for global image handle
            capture_image = VideoOCX.GetColorImageHandle
            ' result_image = VideoOCX_Processed.GetColorImageHandle
    
            Timer1.Enabled = True 'Start capture timer
    
            ' Start Capture mode
            If (Not VideoOCX.Start) Then
                ' Start failed. Display error message and end sub
                MsgBox VideoOCX.GetLastErrorString, vbOKOnly, "VideoOCX Error"
                End
            End If
        End If
    Else
        Start.Caption = "Start"
        Timer1.Enabled = False  'Stop Timer
        VideoOCX.Stop
        VideoOCX.Close
    End If
    
End Sub

Private Sub Timer1_Timer()
    ' Timer for capturing - handles videoOCXTools
    Dim matrix As Variant
    Dim height, width As Integer
    Dim r, c As Integer
    Dim max_r, max_c As Integer
    Dim max_red As Integer
    Dim gain, offset As Variant
    Dim h_cm As Variant
    Dim range As Integer
    Dim pixels_from_center As Integer
    
    ' Calibrated parameter for pixel to distance conversion
    gain = 0.0024259348
    offset = -0.056514344
    h_cm = 5.842
    
    max_red = 0
    
    ' Capture an image
    If (VideoOCX.Capture(capture_image)) Then
        
        ' VideoOCX.Show capture_image
        
        ' Matrix transformation initialization
        matrix = VideoOCX.GetMatrix(capture_image)
        
        height = VideoOCX.GetHeight
        width = VideoOCX.GetWidth
        
        ' Image processing code
        
        ' The laser dot should not be seen above the middle row (with a little pad)
        For r = height / 2 - 20 To height - 1
            
            ' Our physical setup is roughly calibrated to make the laser
            ' dot in the middle columns...dont bother lookng too far away
            For c = width / 2 - 25 To width / 2 + 24
        
                ' Look for the largest red pixel value in the scene (red laser)
                If (matrix(c, r, 2) > max_red) Then
                    max_red = matrix(c, r, 2)
                    max_r = r
                    max_c = c
                End If
            Next c
        Next r
        
        ' Calculate the distance for the laser dot from middle of frame
        pixels_from_center = max_r - 120

' Calculate range in cm based on calibrated parameters
        range = h_cm / Tan(pixels_from_center * gain + offset)

' Print laser dot position row and column to screen
        row_val.Caption = max_r
        col_val.Caption = max_c
        
        ' Print range to laser illuminated object to screen
        range_val.Caption = range
        
        ' Draw a red vertical line to intersect target
        For r = 0 To height - 1
            matrix(max_c, r, 2) = 255
        Next r
        
        ' Draw a red horizontal line to intersect target
        For c = 0 To width - 1
            matrix(c, max_r, 2) = 255
        Next c
        
        VideoOCX.ReleaseMatrixToImageHandle (capture_image)RoboticFan
        
    End If
    
    VideoOCX.Show capture_image

End Sub

截屏如下:

### Visual C++

我的代码是基于Paul Oh教授的教程。

你需要注意，当跟进这个教程的时候，一些必要的文件也许不再正常连接或丢失，他们可以在下面的位置下载。

qcsdk.exe

qc543enu.exe

根据 TRIPOD 的教程的说明，可以在其源程序中插入一段用户自己的图像处理代码，在这里，我插入了下面的代码:

void CTripodDlg::doMyImageProcessing(LPBITMAPINFOHEADER lpThisBitmapInfoHeader)
{
 // doMyImageProcessing:  This is where you'd write your own image processing code
 // Task: Read a pixel's grayscale value and process accordingly

unsigned int W, H;   // Width and Height of current frame [pixels]
 unsigned int    row, col;  // Pixel's row and col positions
 unsigned long   i;   // Dummy variable for row-column vector
 unsigned int max_row;  // Row of the brightest pixel
 unsigned int max_col;  // Column of the brightest pixel
        BYTE  max_val = 0;         // Value of the brightest pixel

// Values used for calculating range from captured image data
 // these values are only for a specific camera and laser setup
 const double gain = 0.0024259348; // Gain Constant used for converting
      // pixel offset to angle in radians
 const double offset = -0.056514344; // Offset Constant
 const double h_cm = 5.842;  // Distance between center of camera and laser
        double  range;          // Calculated range 
 unsigned int pixels_from_center; // Brightest pixel location from center
      // not bottom of frame
 
 char  str[80];         // To print message
 CDC  *pDC;   // Device context need to print message

RoboticFan

W = lpThisBitmapInfoHeader->biWidth; // biWidth: number of columns
        H = lpThisBitmapInfoHeader->biHeight; // biHeight: number of rows
 
 for (row = 0; row < H; row++) {
  for (col = 0; col < W; col++) {

// Recall each pixel is composed of 3 bytes
   i = (unsigned long)(row*3*W + 3*col);
   
   // If the current pixel value is greater than any other, it is the new max pixel
   if (*(m_destinationBmp + i) >= max_val) 
   {
    max_val = *(m_destinationBmp + i);
    max_row = row;
    max_col = col;
   }

}
 }
 // After each frame, reset max pixel value to zero
        max_val = 0;

for (row = 0; row < H; row++) {
  for (col = 0; col < W; col++) {

i = (unsigned long)(row*3*W + 3*col);
   
   // Draw a white cross-hair over brightest pixel in the output display
   if ((row == max_row) || (col == max_col)) 
    *(m_destinationBmp + i) = 
    *(m_destinationBmp + i + 1) = 
    *(m_destinationBmp + i + 2) = 255;

}
 }

// Calculate distance of brightest pixel from center rather than bottom of frame
        pixels_from_center = 120 - max_row;

// Calculate range in cm based on bright pixel location, and setup specific constants
 range = h_cm / tan(pixels_from_center * gain + offset);

// To print message at (row, column) = (75, 580)
 pDC = GetDC();

// Display frame coordinates as well as calculated range
 sprintf(str, "Max Value at x= %u, y= %u, range= %f cm    ",max_col, max_row, range);
 pDC->TextOut(75, 580, str);
 ReleaseDC(pDC);
}

完整的代码可以在下面下载到：
LaserRange.zip

可执行文件可在下面下载到：
LaserRange.exe

注意，为了执行这个文件，你可能需要qcsdk和qc543这两个驱动文件。

下面是摄像头激光测距仪的工作截图，注意它是如何工作的。在第二个例子中，有两个激光点，其中的一个是激光点在摄像头里面的反射，这个反射点由于没有那么强烈的，所以不适用于运算法则。

### 将来的工作

一个重要的改进就是将点改为线，这样可以计算每个光柱的距离而不是单个的光柱。这样的设置可以使车辆能够探测最大的前进距离，同样的，障碍物的最小距离也可以被探测到。

### 相关链接：

此文的英文原文可以在emtionmk的blog找到：英文原文

/*最后非常感谢Rockets的翻译，为大家带来这么高质量的一篇技术文档*\

英文原文：

DIY laser rangefinder

摘译：http://www.pages.drexel.edu/~twd25/webcam_laser_ranger.html 原文: Webcam Based DIY Laser Rangefinder Introduction There are many off the shelf range finding components available including ultrasonic, infrared, and even laser rangefinders. All of these devices work well, but in the field of aerial robotics, weight is a primary concern. It is desirable to get as much ality out of each component that is added to an air. Miniature robotic rotorcraft for example can carry about 100g of payload. It is possible to perform machine vision tasks such as obstacle identification and avoidance though the use of a webcam (or mini wireless camera interfaced to a computer via USB adaptor). Better yet, two webcams can provide stereo machine vision thus improving obstacle avoidance because depth can be determined. The drawback of this of course is the addition of the weight of a second camera. This page describes how a mini laser pointer can be configured along with a single camera to provide mono-machine vision with range information. This project is greatly based on a tutorial found here Theory of Operation The diagram below shows how projecting a laser dot onto a target that is in the field of view of a camera, the distance to that target may be calculated. The math is very simple, so this technique works very well for machine vision applications that need to run quickly. So, here is how it works. A laser-beam is projected onto an object in the field of view of a camera. This laser beam is ideally parallel to the optical axis of the camera. The dot from the laser is captured along with the rest of the scene by the camera. A simple algorithm is run over the image looking for the brightest pixels. Assuming that the laser is the brightest area of the scene (which seems to be true for my dollar store laser pointer indoors), the dots position in the image is known. Then we need to calculate the range to the object based on where along the y axis of the image this laser dot falls. The closer to the center of the image, the farther away the object is. As we can see from the diagram earlier in this section, distance (D) may be calculated: Of course, to solve this equation, you need to know h, which is a constant fixed as the distance between your laser pointer and camera, and theta. Theta is calculated: Put the two above equations together, we get: OK, so the number of pixels from the center of the focal plane that the laser dot appears can just be counted from the image. What about the other parameters in this equation? We need to perform a calibration to derive these. To calibrate the system, we will collect a series of measurements where I know the range to the target, as well as the number of pixels the dot is from the center of the image each time. This data is below: Calibration Data pixels from center actual D (cm) 103 29 81 45 65 58 55 71 49 90 45 109 41 127 39 159 37 189 35 218 Using the following equation, we can calculate the actual angle based on the value of h as well as actual distance for each data point. Now that we have a Theta_actual for each value, we can come up with a relationship that lets us calculate theta from the number of pixels from image center. I used a linear relationship (thus a gain and offset are needed). This seems to work well even though it does not account for the fact that the focal plane is a plane rather than curved at a constant radius around the center of the lens. From my calibration data, I calculated: Offset (ro) = -0.056514344 radians Gain (rpc) = 0.0024259348 radians/pixel Using: I solved for calculated distances, as well as error from actual distance from the calibration data: Actual and Calculated Range Data pixels from center calc D (cm) actual D (cm) % error 103 29.84 29 2.88 81 41.46 45 -7.87 65 57.55 58 -0.78 55 75.81 71 6.77 49 93.57 90 3.96 45 110.85 109 1.70 41 135.94 127 7.04 39 153.27 159 -3.60 37 175.66 189 -7.06 35 205.70 218 -5.64 Components There are not a lot of parts in my sample range finder. I used a piece of cardboard to hold a laser pointer to a webcam so that the laser pointer points in a direction that is parallel to that of the camera. The parts seen below are laid out on a one inch grid for reference. My assembled range finder looks like this: Software I have written software two ways, one using visual c++ and the other using visual basic. You will probably find that the visual basic version of the software is much easier to follow than the vc++ code, but with everything, there is a tradeoff. The vc++ code can be put together for free (assuming that you have visual studio), while the vb code requires the purchase of a third party software package (also in addition to visual studio). Visual Basic The visual basic code that I have written is available as a package here: vb_laser_ranger.zip For this code to work, you will need the VideoOCX ActiveX component installed on your computer. The code that describes the s found in the main form is seen below: Private Sub exit_Click() ' only if running... If (Timer1.Enabled) Then Timer1.Enabled = False 'Stop Timer VideoOCX.Stop VideoOCX.Close End If End End Sub Private Sub Start_Click() 'Init VideoOCX Control, allocate memory and start grabbing If (Not Timer1.Enabled) Then Start.Caption = "Stop" ' Disable internal error messages in VideoOCX VideoOCX.SetErrorMessages False ' Init control If (Not VideoOCX.Init) Then ' Init failed. Display error message and end sub MsgBox VideoOCX.GetLastErrorString, vbOKOnly, "VideoOCX Error" End Else ' Allocate memory for global image handle capture_image = VideoOCX.GetColorImageHandle ' result_image = VideoOCX_Processed.GetColorImageHandle Timer1.Enabled = True 'Start capture timer ' Start Capture mode If (Not VideoOCX.Start) Then ' Start failed. Display error message and end sub MsgBox VideoOCX.GetLastErrorString, vbOKOnly, "VideoOCX Error" End End If End If Else Start.Caption = "Start" Timer1.Enabled = False 'Stop Timer VideoOCX.Stop VideoOCX.Close End If End Sub Private Sub Timer1_Timer() ' Timer for capturing - handles videoOCXTools Dim matrix As Variant Dim height, width As Integer Dim r, c As Integer Dim max_r, max_c As Integer Dim max_red As Integer Dim gain, offset As Variant Dim h_cm As Variant Dim range As Integer Dim pixels_from_center As Integer ' Calibrated parameter for pixel to distance conversion gain = 0.0024259348 offset = -0.056514344 h_cm = 5.842 max_red = 0 ' Capture an image If (VideoOCX.Capture(capture_image)) Then ' VideoOCX.Show capture_image ' Matrix transformation initialization matrix = VideoOCX.GetMatrix(capture_image) height = VideoOCX.GetHeight width = VideoOCX.GetWidth ' Image processing code ' The laser dot should not be seen above the middle row (with a little pad) For r = height / 2 - 20 To height - 1 ' Our physical setup is roughly calibrated to make the laser ' dot in the middle columns...dont bother lookng too far away For c = width / 2 - 25 To width / 2 + 24 ' Look for the largest red pixel value in the scene (red laser) If (matrix(c, r, 2) > max_red) Then max_red = matrix(c, r, 2) max_r = r max_c = c End If Next c Next r ' Calculate the distance for the laser dot from middle of pixels_from_center = max_r - 120 ' Calculate range in cm based on calibrated parameters range = h_cm / Tan(pixels_from_center * gain + offset) ' Print laser dot position row and column to screen row_val.Caption = max_r col_val.Caption = max_c ' Print range to laser illuminated object to screen range_val.Caption = range ' Draw a red vertical line to intersect target For r = 0 To height - 1 matrix(max_c, r, 2) = 255 Next r ' Draw a red horizontal line to intersect target For c = 0 To width - 1 matrix(c, max_r, 2) = 255 Next c VideoOCX.ReleaseMatrixToImageHandle (capture_image) End If VideoOCX.Show capture_image End Sub Screen shots from this code can be seen below: Visual C++ My code is based closely on a tutorial offered by Dr. Paul Oh. You will notice that while following this TRIPOD tutorial, a few necessary files are no longer properly linked or missing. They may be downloaded from me: qcsdk.exe qc543enu.exe Follow the TRIPOD tutorial, and note how there is a section where you are invited to insert your own code for image processing. In this section, I inserted the following code: void CTripodDlg::doMyImageProcessing(LPBITMAPINFOHEADER lpThisBitmapInfoHeader) { // doMyImageProcessing: This is where you'd write your own image processing code // Task: Read a pixel's grayscale value and process accordingly unsigned int W, H; // Width and Height of current [pixels] unsigned int row, col; // Pixel's row and col positions unsigned long i; // Dummy variable for row-column vector unsigned int max_row; // Row of the brightest pixel unsigned int max_col; // Column of the brightest pixel BYTE max_val = 0; // Value of the brightest pixel // Values used for calculating range from captured image data // these values are only for a specific camera and laser setup const double gain = 0.0024259348; // Gain Constant used for converting // pixel offset to angle in radians const double offset = -0.056514344; // Offset Constant const double h_cm = 5.842; // Distance between center of camera and laser double range; // Calculated range unsigned int pixels_from_center; // Brightest pixel location from center // not bottom of char str[80]; // To print message CDC *pDC; // Device context need to print message W = lpThisBitmapInfoHeader->biWidth; // biWidth: number of columns H = lpThisBitmapInfoHeader->biHeight; // biHeight: number of rows for (row = 0; row < H; row++) { for (col = 0; col < W; col++) { // Recall each pixel is composed of 3 bytes i = (unsigned long)(row*3*W + 3*col); // If the current pixel value is greater than any other, it is the new max pixel if (*(m_destinationBmp + i) >= max_val) { max_val = *(m_destinationBmp + i); max_row = row; max_col = col; } } } // After each , reset max pixel value to zero max_val = 0; for (row = 0; row < H; row++) { for (col = 0; col < W; col++) { i = (unsigned long)(row*3*W + 3*col); // Draw a white cross-hair over brightest pixel in the output display if ((row == max_row) ¦¦ (col == max_col)) *(m_destinationBmp + i) = *(m_destinationBmp + i + 1) = *(m_destinationBmp + i + 2) = 255; } } // Calculate distance of brightest pixel from center rather than bottom of pixels_from_center = 120 - max_row; // Calculate range in cm based on bright pixel location, and setup specific constants range = h_cm / tan(pixels_from_center * gain + offset); // To print message at (row, column) = (75, 580) pDC = GetDC(); // Display coordinates as well as calculated range sprintf(str, "Max Value at x= %u, y= %u, range= %f cm ",max_col, max_row, range); pDC->TextOut(75, 580, str); ReleaseDC(pDC); } My complete code for this project may be downloaded here: LaserRange.zip Or if you would just like to try out the executable, download it here: LaserRange.exe Note, to run this executable, you will need to have both qcsdk and the qc543 driver installed on your computer. Below are two examples of the webcam based laser range finder in action. Note how it looks like there are two laser dots in the second example. This "stray light" is caused by internal reflections in the camera. The reflected dot loses intensity as it bounces within the camera so it does not interfere with the algorithm that detects the brightest pixel in the image. Future Work One specific improvement that can be made to this webcam based laser range finder is to project a horizontal line rather than a dot onto a target. This way, we could calculate the range for each column of the image rather than just one column. Such a setup would be able to be used to locate areas of maximum range as places that a vehicle could steer towards. Likewise, areas of minimum range would be identified as obstacles to be avoided.