一 使ucLinux在DE2开发板上运行起来

由于没有MMU（Memory Management Unit），Nios II处理器不能运行完整的Linux操作系统。ucLinux是专门针对这一类处理器而设计的嵌入式操作系统，其优良特性不用再多说。在进行任何其他实验以前，我们可以先在DE2上运行一个编译好的Nios II系统和ucLinux内核。这是最基本的，也是非常重要的一步。

在开始之前，先在电脑上安装好Quartus 6.0和Nios II EDS 6.0等开发软件，安装好USB-Blaster的驱动。

### For DE2  2C35 dev board

1、从网上下载镜像文件 zImage_de2_net 和工程文件 de2_net_v1.1.zip，保存在开发目录中。我的目录是E:/de2/download。

2、在download文件夹中将de2_net_v1.1.zip解压。

3、打开一个nios2命令行界面。

开始-->所有程序-->Altera-->Nios II EDS 6.0-->Nios II Command Shell。

4、在Nios II Command Shell中，进入E:/de2/download目录。

$ cd e:/de2/download

5、向FPGA中写入配置文件。

$ nios2-configure-sof DE2_NET/DE2_NET.sof

Info:************************************************************

Info: Running Quartus II Programmer

Info: Command: quartus_pgm --no_banner --mode=jtag -o p;DE2_NET/DE2_NET.sof

Info: Using programming cable "USB-Blaster [USB-0]"

Info: Started Programmer operation at Thu Mar 22 14:57:28 2007

Info: Configuring device index 1

Info: Device 1 contains JTAG ID code 0x020B40DD

Info: Configuration succeeded -- 1 device(s) configured

Info: Successfully performed operation(s)

Info: Ended Programmer operation at Thu Mar 22 14:57:31 2007

Info: Quartus II Programmer was successful. 0 errors, 0 warnings

Info: Processing ended: Thu Mar 22 14:57:31 2007

Info: Elapsed time: 00:00:06

/cygdrive/e/de2/download

6、向SDRAM中写入内核镜像文件。

$ nios2-download -g zImage_de2_net

[SOPC Builder]$ nios2-download -g zImage_de2_net

Using cable "USB-Blaster [USB-0]", device 1, instance 0x00

Pausing target processor: OK

Initializing CPU cache (if present)

OK

Downloaded 1198KB in 18.1s (66.1KB/s)

Verified OK

Starting processor at address 0x00500000

/cygdrive/e/de2/download

7、启动内核

$ nios2-terminal

nios2-terminal: connected to hardware target using JTAG UART on cable

nios2-terminal: "USB-Blaster [USB-0]", device 1, instance 0

nios2-terminal: (Use the IDE stop button or Ctrl-C to terminate)

Uncompressing Linux... Ok, booting the kernel.

Linux version 2.6.19-uc1 (hippo@darkstar) (gcc version 3.4.6) #8 PREEMPT Fri Feb

9 11:52:57 CST 2007

uClinux/Nios II

Altera Nios II support (C) 2004 Microtronix Datacom Ltd.

setup_arch: No persistant network settings signature at 008F0000

Built 1 zonelists.  Total pages: 2032

Kernel command line:

PID hash table entries: 32 (order: 5, 128 bytes)

Dentry cache hash table entries: 1024 (order: 0, 4096 bytes)

Inode-cache hash table entries: 1024 (order: 0, 4096 bytes)

Memory available: 5948k/8192k RAM, 0k/0k ROM (1469k kernel code, 685k data)

Mount-cache hash table entries: 512

NET: Registered protocol family 16

NET: Registered protocol family 2

IP route cache hash table entries: 1024 (order: 0, 4096 bytes)

TCP established hash table entries: 1024 (order: 0, 4096 bytes)

TCP bind hash table entries: 1024 (order: 0, 4096 bytes)

TCP: Hash tables configured (established 1024 bind 1024)

TCP reno registered

io scheduler noop registered

io scheduler deadline registered (default)

Serial: JTAG UART driver $Revision: 1.3 $

ttyJ0 at MMIO 0x81004000 (irq = 1) is a jtag_uart

<DM9KS> I/O: 80900090, VID: 90000a46

TCP cubic registered

NET: Registered protocol family 1

NET: Registered protocol family 17

Freeing unused kernel memory: 572k freed (0x17c000 - 0x20a000)

Shell invoked to run file: /etc/rc

Command: hostname uClinux

Command: mount -t proc proc /proc

Command: mount -t sysfs sysfs /sys

Command: mount -t usbfs none /proc/bus/usb

mount: Mounting none on /proc/bus/usb failed: No such file or directory

Command: mkdir /var/tmp

Command: mkdir /var/log

Command: mkdir /var/run

Command: mkdir /var/lock

Command: mkdir /var/empty

Command: ifconfig lo 127.0.0.1

Command: route add -net 127.0.0.0 netmask 255.0.0.0 lo

Command: cat /etc/motd

Welcome to

____ _  _

/  __| ||_|

_   _| |  | | _ ____  _   _  _  _

| | | | |  | || |  _ /| | | |/ // /

| |_| | |__| || | | | | |_| |/    /

|  ___/____|_||_|_| |_|/____|/_//_/

| |

|_|

For further information check:

http://www.uclinux.org/

Execution Finished, Exiting

Sash command shell (version 1.1.1)

/>

看到这个信息，就说明ucLinux已经成功的在系统中运行了，接下来可以试验一些shell命令:

/> ifconfig eth0 up

/> dhcpcd & get network config from a dhcp server, eg, ip,gateway,nameserver

[19]

/> ifconfig

eth0      Link encap:Ethernet  HWaddr 00:07:ED:00:00:00

inet addr:192.168.10.131  Bcast:192.168.10.255  Mask:255.255.255.0

UP BROADCAST NOTRAILERS RUNNING MULTICAST  MTU:1500  Metric:1

RX packets:22 errors:0 dropped:0 overruns:0 frame:0

TX packets:4 errors:0 dropped:0 overruns:0 carrier:0

collisions:0 txqueuelen:1000

RX bytes:5054 (4.9 KiB)  TX bytes:1830 (1.7 KiB)

Interrupt:8

lo        Link encap:Local Loopback

inet addr:127.0.0.1  Mask:255.0.0.0

UP LOOPBACK RUNNING  MTU:16436  Metric:1

RX packets:0 errors:0 dropped:0 overruns:0 frame:0

TX packets:0 errors:0 dropped:0 overruns:0 carrier:0

collisions:0 txqueuelen:0

RX bytes:0 (0.0 B)  TX bytes:0 (0.0 B)

/> inetd & # start inetd to invoke telnetd and ftpd services

[22]

/> boa & # start httpd with cgi-demo

[23]

/> netstat –a # show network services

Active Internet connections (servers and established)

Proto Recv-Q Send-Q Local Address         Foreign Address         State

tcp        0      0 *:http               *:*                    LISTEN

tcp        0      0 *:ftp                *:*                    LISTEN

tcp        0      0 *:telnet              *:*                    LISTEN

Active UNIX domain sockets (servers and established)

Proto RefCnt Flags       Type       State         I-Node Path

/> TZ=CST-8  # my time zone
/> ntpdate pool.ntp.org  # get date and time from ntp server

Looking for host pool.ntp.org and service ntp

host found : sland.agava.net

Clock: old time 1999/11/30 - 00:17:35 GMT

Clock: new time 2007/03/22 - 07:21:03 GMT

22 Mar 15:21:03 ntpdate[25]: step time server 89.108.81.77 offset 230627007.9839

16 sec

/> free

MemTotal:         6520 kB

MemFree:          4332 kB

Buffers:             0 kB

/> ps

PID PORT STAT  SIZE SHARED %CPU COMMAND

1      S     147K     0K  0.3 /init

2      S       0K     0K  0.0 ksoftirqd/0

3      S       0K     0K  0.0 events/0

4      S       0K     0K  0.0 khelper

5      S       0K     0K  0.0 kthread

6      S       0K     0K  0.0 kblockd/0

7      S       0K     0K  0.0 pdflush

8      S       0K     0K  0.0 pdflush

9      S       0K     0K  0.0 kswapd0

10      S       0K     0K  0.0 aio/0

17      R     147K     0K  0.0 -/bin/sh

19      S     147K     0K  0.0 dhcpcd

22      S      95K     0K  0.0 inetd

23      S     275K     0K  0.1 boa

/>

看用这种方法sof 和 zImage并没有写入到cfi flash或epcs中，调电后这些信息会丢失。关于如何将sof和zImage写入到flash中调电后不丢失的方法，将在后文中详述。