;***************************************************************************

i2c_rep_start:

sbi	DDRB,SCLK		; force SCL low

rcall	i2c_qp_delay		; quarter period delay

cbi	DDRB,SDIN		; release SDA

rcall	i2c_hp_delay		; half period delay

cbi	DDRB,SCLK		; release SCL

rcall	i2c_qp_delay		; quarter period delay

;***************************************************************************

i2c_start:

sbi	DDRB,SDIN		; force SDA low

rcall	i2c_qp_delay		; quarter period delay

;***************************************************************************

i2c_write:

sec				; set carry flag

rol	acc			; shift in carry and out bit one

rjmp	i2c_write_first

i2c_write_bit:

lsl	acc			; if transmit register empty

i2c_write_first:

breq	i2c_get_ack		;	goto get acknowledge

sbi	DDRB,SCLK		; force SCL low

rcall	i2c_qp_delay

brcc	i2c_write_low		; if bit high

nop				;	(equalize number of cycles)

cbi	DDRB,SDIN		;	release SDA

rjmp	i2c_write_high

i2c_write_low:				; else

sbi	DDRB,SDIN		;	force SDA low

rjmp	i2c_write_high		;	(equalize number of cycles)

i2c_write_high:

rcall	i2c_hp_delay		; half period delay

cbi	DDRB,SCLK		; release SCL

rcall	i2c_hp_delay		; half period delay

sbis	PINB,SCLK		; wait SCL high 07-12-19

rjmp	pc-1

rjmp	i2c_write_bit

;***************************************************************************

i2c_get_ack:

sbi	DDRB,SCLK		; force SCL low

cbi	DDRB,SDIN		; release SDA

rcall	i2c_hp_delay		; half period delay

cbi	DDRB,SCLK		; release SCL

i2c_get_ack_wait:

sbis	PINB,SCLK		; wait SCL high

;(In case wait states are inserted)

rjmp	i2c_get_ack_wait

clc				; clear carry flag

sbic	PINB,SDIN		; if SDA is high

sec				;	set carry flag

rcall	i2c_hp_delay		; half period delay

ret

;***************************************************************************

i2c_read:

;rol	i2cstat			; store acknowledge

; (used by i2c_put_ack)

ldi	acc,0x01		; data = 0x01

i2c_read_bit:				; do

sbi	DDRB,SCLK		; 	force SCL low

cbi	DDRB,SDIN

rcall	i2c_hp_delay		;	half period delay

cbi	DDRB,SCLK		;	release SCL

rcall	i2c_hp_delay		;	half period delay

sbis	PINB,SCLK		; wait SCL high 07-12-19

rjmp	pc-1

clc				;	clear carry flag

sbic	PINB,SDIN		;	if SDA is high

sec				;		set carry flag

rol	acc			; 	store data bit

brcc	i2c_read_bit		; while receive register not full

;***************************************************************************

i2c_put_ack:

sbi	DDRB,SCLK		; force SCL low

;ror	i2cstat			; get status bit

brtc	i2c_put_ack_low		; if bit low goto assert low

cbi	DDRB,SDIN		;	release SDA

clt

rjmp	i2c_put_ack_high

i2c_put_ack_low:			; else

sbi	DDRB,SDIN		;	force SDA low

i2c_put_ack_high:

rcall	i2c_hp_delay		; half period delay

cbi	DDRB,SCLK		; release SCL

i2c_put_ack_wait:

sbis	PINB,SCLK		; wait SCL high

rjmp	i2c_put_ack_wait

rcall	i2c_hp_delay		; half period delay

ret

;***************************************************************************

i2c_stop:

sbi	DDRB,SCLK		; force SCL low

sbi	DDRB,SDIN		; force SDA low

rcall	i2c_hp_delay		; half period delay

cbi	DDRB,SCLK		; release SCL

rcall	i2c_qp_delay		; quarter period delay

cbi	DDRB,SDIN		; release SDA

rcall	i2c_hp_delay		; half period delay

ret

;***************************************************

i2c_hp_delay:			;call process: 2us

nop

nop

nop

nop

nop

nop

nop

nop

nop

nop

nop

nop

nop

nop

i2c_qp_delay:			;call process: 2us

nop

nop

nop

nop

nop

nop

nop

nop

nop

nop

ret