nutCamera command interface

- X = What ever you want

- cam_res_t typedef:

typedef struct  {

#define CAM_SUCCESS		0x85	// successful

#define CAM_ERROR			0x01	// failed

#define CAM_NOT_SUP		0x02	// not supported

uint32	rp;

} cam_res_t;

Table 1.  nutCamera command

| Command | Command value | Brief | Para(uint32) | Response(uint32) |
| --- | --- | --- | --- | --- |
|  |  |  | Bit[31:24] | Bit[23:16] | Bit[15:8] | Bit[7:0] |  |
| CAM_OPEN | 0x10 | Open an image | X | Image size in byte |
| CAM_LSEEK | 0x11 | Move the internal pointer | Offset from top of the image(left top) | cam_res_t |
| CAM_READ | 0x12 | Read image | Number of bytes to read | Datas |
| CAM_CLOSE | 0x13 | Close an image | X | cam_res_t |
| CAM_RGB | 0x30 | RGB565 mode | X | cam_res_t |
| CAM_BW | 0x31 | Black and white mode | X | cam_res_t |
| CAM_VGA | 0x32 | VGA mode (640 * 480) | X | cam_res_t |
| CAM_QVGA | 0x33 | QVGA mode (320 * 240) | X | cam_res_t |
| CAM_CIF | 0x34 | CIF mode (176 * 144) | X | cam_res_t |
| CAM_SET_CFG | 0x4e | Write camera register | Value | Address | cam_res_t |
| CAM_GET_CFG | 0x4f | Read camera register | Address | Value |
| CAM_EC | 0x50 | Exposure control | 1 = Auto 0 = Manu | X | X | Exposure value | cam_res_t |
| CAM_WB | 0x51 | White banlance | 1 = Auto 0 = Manu | Red value | X | Blue Value | cam_res_t |
| CAM_LCD | 0x70 | Enable/Diable Nokia LCD interface | 1 = Enable 0 = Disable | cam_res_t |
| CAM_SPI_CFG | 0x71 | Config SPI baudrate | Baudrate | cam_res_t |
| CAM_US_CFG | 0x72 | Config USART baudrate | Baudrate | cam_res_t |