#### 说明黄绿色底纹一般都要用到，灰色底纹如果出现同样的问题才用到，不出现类似问题，则跳过

#### 硬件配置

BeagleBoard Rev.B7 主要硬件配置介绍如下。

##### Package on Package POP CPU/Memory chip

- TI OMAP3530 Processor - 720 MHz ARM Cortex-A8 core

- 'HD capable' TMS320C64x+ core (520MHz upto 720p@30fps)

- Imagination Technologies PowerVR SGX 2D/3D graphics processor

- 128 MB LPDDR RAM memory

- 256 MB NAND Flash memory

##### 外围接口

- DVI-D, USB OTG， SD/MMC card slot

- Stereo in and out jacks

- Power socket

- RS232 port

- JTAG connector

- reset 按钮

##### 启动方式

- Boot code stored in ROM

- Boot from NAND memory, SD/MMC, USB 或者串口

#### 连线

Beagle Board 的使用如下图所示：

除了 Beagle Board 开发板之外，还需自己配置：

- 5V 电源一个，内正外负

- OTG 转 usb 母口线一根

- 有源 USB HUB

- HDMI 转 DVI 线一根

- usb 口键盘、usb口鼠标

##### 启动流程

一般来讲，bealgeboard 启动流程如下所示：

bootrom（内部ram）--->xloader（内部ram）---->uboot（外部ram）---->kernel（外部ram）

以上为大体了解一下beageleboard

以下为具体移植过程：

主机配置要求：

Android在pc开发环境是基于Ubuntu，请安装Ubuntu10.04或更高版本。主机安装Android的需要几个具体的依赖，这些都可以使用下面的命令通过网络动态地安装。

### For Ubuntu on 32-bit machines

$ sudo add-apt-repository "deb http://archive.canonical.com/ lucid partner"

$ sudo add-apt-repository "deb-src http://archive.canonical.com/ubuntu lucid partner"

$ sudo apt-get update

$ sudo apt-get install git-core gnupg sun-java6-jdk flex bison gperf libsdl-dev libesd0-dev libwxgtk2.6-dev build-essential zip curl libncurses5-dev zlib1g-dev minicom tftpd uboot-mkimage expect

$ sudo update-java-alternatives -s java-6-sun

注意：Android Gingerbread（2.3）需要在Ubuntu的Java 6，而以前的版本升级Froyo（2.2）是使用Java 5。

如果你使用$sudo update-java-alternatives -s java-6-sun命令出现下面的语句

alex@alex-home:~$ sudo update-java-alternatives -s java-6-sun

update-alternatives: error: no alternatives for mozilla-javaplugin.so.

update-alternatives: error: no alternatives for xulrunner-1.9-javaplugin.so.

update-alternatives: error: no alternatives for mozilla-javaplugin.so.

update-alternatives: error: no alternatives for xulrunner-1.9-javaplugin.so.

试试下面的方法：

alex@alex-home:~$ java -version

java version "1.6.0_22"

Java(TM) SE Runtime Environment (build 1.6.0_22-b04)

Java HotSpot(TM) 64-Bit Server VM (build 17.1-b03, mixed mode)

alex@alex-home:~$

alex@alex-home:~$ sudo update-alternatives --config java

There are 2 choices for the alternative java (providing /usr/bin/java).

Selection    Path                                      Priority   Status

------------------------------------------------------------

0            /usr/lib/jvm/java-6-openjdk/jre/bin/java   1061      auto mode

* 1            /usr/lib/jvm/java-6-sun/jre/bin/java       63        manual mode

按回车键保留当前的选择（*）或者打出选中的数字（比如这个就是1）

虽然JDK 不在列表里面, 但它在硬盘列表中:

alex@alex-home:~$ ls /usr/lib/jvm/

default-java  java-1.6.0-openjdk  java-6-openjdk  java-6-sun  java-6-sun-1.6.0.22

更新:

Installing plugin and fonts caused update-java-alternatives to stop complaining, but still no luck:

$sudo apt-get install sun-java6-plugin sun-java6-fonts

Then:

alex@alex-home:~$ sudo update-java-alternatives -s java-6-sun

alex@alex-home:~$ java -version

java version "1.6.0_22"

Java(TM) SE Runtime Environment (build 1.6.0_22-b04)

Java HotSpot(TM) 64-Bit Server VM (build 17.1-b03, mixed mode)

Source locations

TI 为所有的Android支持的设备提供多种源，开发人员可以从gitorious.org/rowboat下载源或使用pre-packaged repo在DevKit。这里我们只提供如何从 Gitorious.org/rowboat 获取资源的方法。

Using gitorious.org/rowboat

下面的命令帮助开发者从 Gitorious.org/rowboat 获取资源

$ mkdir rowboat-android

$ cd rowboat-android

$ repo init -u git://gitorious.org/rowboat/manifest.git -m TI-Android-GingerBread-2.3-DevKit-1.0.xml

$ repo sync

这将生成以下源

- Android 文件系统

- Android Linux Kernel (在 kernel 路径下)

- u-boot boot loader (在 u-boot-omap3路径下)

- x-loader (在 x-load-omap3路径下)

- Toolchain (prebuilt/linux-x86/toolchain/arm-eabi-4.3.1/bin)

Tool chain 设置

设置prebuilt/linux-x86/toolchain/arm-eabi-4.3.1/bin为交叉编译器的环境变量

$export PATH=rowboat-android/prebuilt/linux-x86/toolchain/arm-eabi-4.3.1/bin:$PATH

编译 procedure

- 编译 x-loader

运行以下命令

$ make CROSS_COMPILE=arm-eabi- distclean

$ make CROSS_COMPILE=arm-eabi- omap3beagle_config

$ make CROSS_COMPILE=arm-eabi-

此命令将x-loader Image 编译成"x-load.bin"

创建MLO文件为MMC / SD卡开机使用，使用signGP工具标记x-loader， signGP工具在Tools/signGP目录中找到。

$ ./signGP ./x-load.bin

signGP 工具将创建一个.ift 文件, 重命名 x-load.bin.ift 为 MLO

$ mv x-load.bin.ift MLO

编译 boot loader (u-boot)

- 切换路径到 u-boot-omap3

$ cd u-boot-omap3

运行以下命令编译u_boot

$ make CROSS_COMPILE=arm-eabi- distclean

$ make CROSS_COMPILE=arm-eabi- omap3_beagle_config

$ make CROSS_COMPILE=arm-eabi-

这个命令将生成 u-boot Image "u-boot.bin"

编译 Linux kernel

- 切换路径到kernel

$ cd kernel

运行以下命令编译 sources

$ make CROSS_COMPILE=arm-eabi- distclean

$ make CROSS_COMPILE=arm-eabi- omap3_beagle_android_defconfig

$ make CROSS_COMPILE=arm-eabi- uImage

这个命令将生成 uImage (kernel image) 在 kernel/arch/arm/boot 文件夹

编译 Android 文件系统

- 编译根文件系统

$ make TARGET_PRODUCT=beagleboard -j8 OMAPES=3.x

Prepare the root filesystem:

$ cd out/target/product/ beagleboard

$sudo ../../../../build/tools/mktarball.sh ../../../host/linux-x86/bin/fs_get_stats android_rootfs . rootfs rootfs.tar.bz2

rootfs.tar.bz2 就是 android 文件系统, 它能被放入 SD/MMC 卡或者用在 our NFS.

LinuxBootDiskFormat

- 如何创建一个BeagleBoard双分区卡从第一个分区启动Linux，并在第二个分区有根文件系统。

Details

Determine which device the SD Card Reader is on your system

SD卡插入你的读卡器，然后插入你的pc，执行下列操作以确定哪个设备它在你的系统上。

$ dmesg | tai 
... 
[ 6854.215650] sd 7:0:0:0: [sdb] Mode Sense: 0b 00 00 08 
[ 6854.215653] sd 7:0:0:0: [sdb] Assuming drive cache: write through 
[ 6854.215659]  sdb: sdb1 
[ 6854.218079] sd 7:0:0:0: [sdb] Attached SCSI removable disk 
[ 6854.218135] sd 7:0:0:0: Attached scsi generic sg2 type 0

这种情况下它会显示 /dev/sdb

请检查是否已安装了自动挂载SD卡

注意可能有多个分区（在下面的例子所示只有一个）。

$ [df -h] 
Filesystem            Size  Used Avail Use% Mounted on 
... 
/dev/sdb1             400M   94M  307M  24% /media/disk 
...

注意 "Mounted on" 作用在上面的sdb1上 ，需要使用 umount 命令如下.

If so, unmount it

$ umount /media/disk

Start fdisk

一定要选择整个设备（/ dev/ sdb的），而不是单个分区（/ dev/sdb1）$ sudo fdisk /dev/sdb

打印分区记录

因此，你知道你的starting point。请务必写下卡片上的字节数(在本例中, 2021654528).

Command (m for help): p 
 
Disk /dev/sdb: 2021 MB, 2021654528 bytes 
255 heads, 63 sectors/track, 245 cylinders 
Units = cylinders of 16065 * 512 = 8225280 bytes 
 
   Device Boot      Start         End      Blocks   Id  System 
/dev/sdb1   *           1         246     1974240+   c  W95 FAT32 (LBA) 
Partition 1 has different physical/logical endings: 
     phys=(244, 254, 63) logical=(245, 200, 19)

删除所有的已有分区

Command (m for help): d
Selected partition 1

Set the Geometry of the SD Card

如果上面的打印信息显示的不是 255 heads, 63 sectors/track, 执行以下步骤以expert mode重做sd卡

- 进入 expert mode.

Command (m for help): x

- 设置 the number of heads to 255.

Expert Command (m for help): h 
Number of heads (1-256, default xxx): 255

- 设置 the number of sectors to 63.

Expert Command (m for help): s 
Number of sectors (1-63, default xxx): 63

- 为你的sd卡计算 the number of Cylinders

#cylinders = FLOOR (the number of Bytes on the SD Card (from above) / 255 / 63 / 512 ) 
 
这个例子是、:  2021654528 / 255 / 63 / 512 = 245.79.  因此我们使用 245 (取整).

- 设置 the number of cylinders 用计算出来的数字.

Expert Command (m for help): c 
Number of cylinders (1-256, default xxx): [enter the number you calculated]

- 返回正常模式

Expert Command (m for help): r

打印分区记录检查你的工作

Command (m for help): p 
 
Disk /dev/sdb: 2021 MB, 2021654528 bytes 
255 heads, 63 sectors/track, 245 cylinders 
Units = cylinders of 16065 * 512 = 8225280 bytes 
 
   Device Boot      Start         End      Blocks   Id  System

#### Create the FAT32 partition for booting and transferring files from Windows

Command (m for help): n 
Command action 
   e   extended 
   p   primary partition (1-4) 
p 
Partition number (1-4): 1 
First cylinder (1-245, default 1): (press Enter) 
Using default value 1 
Last cylinder or +size or +sizeM or +sizeK (1-245, default 245): +50 
 
Command (m for help): t 
Selected partition 1 
Hex code (type L to list codes): c
Changed system type of partition 1 to c (W95 FAT32 (LBA))

#### Mark it as bootable

Command (m for help): a 
Partition number (1-4): 1

#### Create the Linux partition for the root file system

Command (m for help): n 
Command action 
   e   extended 
   p   primary partition (1-4) 
p 
Partition number (1-4): 2 
First cylinder (52-245, default 52): (press Enter) 
Using default value 52 
Last cylinder or +size or +sizeM or +sizeK (52-245, default 245): (press Enter) 
Using default value 245

#### Print to Check Your Work

Command (m for help): p 
 
Disk /dev/sdb: 2021 MB, 2021654528 bytes 
255 heads, 63 sectors/track, 245 cylinders 
Units = cylinders of 16065 * 512 = 8225280 bytes 
 
   Device Boot      Start         End      Blocks   Id  System 
/dev/sdb1   *           1          51      409626    c  W95 FAT32 (LBA) 
/dev/sdb2              52         245     1558305   83  Linux

保存在SD卡中的新的分区记录
这是一个重要步骤。所有的工作到目前为止只是暂时的

Command (m for help): w 
The partition table has been altered! 
 
Calling ioctl() to re-read partition table. 
 
WARNING: Re-reading the partition table failed with error 16: Device or resource busy. 
The kernel still uses the old table. 
The new table will be used at the next reboot. 
 
WARNING: If you have created or modified any DOS 6.x 
partitions, please see the fdisk manual page for additional 
information. 
Syncing disks.

#### 格式化分区

这些命令给出两个分区的卷名称Label1和Label2。您也可以替换你自己的卷标。

$ sudo mkfs.msdos -F 32 /dev/sdb1 -n LABEL1 
mkfs.msdos 2.11 (12 Mar 2005) 
 
$ sudo mkfs.ext3 -L LABEL2 /dev/sdb2 
mke2fs 1.40-WIP (14-Nov-2006) 
Filesystem label= 
OS type: Linux 
Block size=4096 (log=2) 
Fragment size=4096 (log=2) 
195072 inodes, 389576 blocks 
19478 blocks (5.00%) reserved for the super user 
First data block=0 
Maximum filesystem blocks=402653184 
12 block groups 
32768 blocks per group, 32768 fragments per group 
16256 inodes per group 
Superblock backups stored on blocks:  
        32768, 98304, 163840, 229376, 294912 
 
Writing inode tables: done                             
Creating journal (8192 blocks): done 
Writing superblocks and filesystem accounting information:

生成的SD/ MMC卡来引导Android

上面编译好的 Images 拷贝到 SD / MMC 卡里去引导 Android

然后，将 MLO，u-boot.bin 和 uImage 拷到 SD 卡的第一个分区(FAT32)，注意要严格按照上面的先后顺序拷贝，MLO 必须在第一扇区。

$ cp x-loader-03.00.02.07/MLO /dev/sdb1

$ cp u-boot-omap3/u-boot.bin /dev/sdb1

$ cp kernel/arch/arm/boot/uImage /dev/sdb1

将 root 文件系统拷入 SD 卡的第二个分区并解压：

$ cp out/target/product/beagleboard/rootfs.tar.bz2 /dev/sdb2

$ sudo tar -jxvf rootfs.tar.bz2

$ sudo rm rootfs.tar.bz2

用新立得软件搜索Gtkterm并下载更新安装，这时它将在应用下的附件的子菜单中出现名字为serial port terminal

SD 卡插入 beagle board，打开Gtkterm找到配置菜单下面的子菜单port按如下参数配置 Gtkterm，其他皆为默认即可：

Port: /dev/ttyUSB0

Speed: 115200

插上电源开机，进入如下所示的命令行：

Texas Instruments X-Loader 1.41

Starting OS Bootloader...

U-Boot 1.3.3 (Jul 10 2008 - 16:33:09)

OMAP3530-GP rev 2, CPU-OPP2 L3-165MHz

OMAP3 Beagle Board + LPDDR/NAND

DRAM:  128 MB

NAND:  256 MiB

In:    serial

Out:   serial

Err:   serial

Audio Tone on Speakers  ... complete

OMAP3 beagleboard.org #

依次运行如下命令：

/* Download Image */

mmcinit

fatload mmc 0 0x80300000 uImage

/* set boot args */

setenv bootargs console=ttyS2,115200n8 noinitrd root=/dev/mmcblk0p2 rootfstype=ext3 rw rootwait omapfb.video_mode=1024x768MR-16@60

/* boot kernel image*/

bootm 0x80300000