### Specification

| Global Part Number | ENC-03M | ENC-03R | ENC-03J |
| --- | --- | --- | --- |
| Previous Part Number |  |  |  |
| Supply Voltage | 2.7 to 5.25 Vdc | 2.7 to 5.25 Vdc | 2.7 to 5.5 Vdc |
| Current Consumption (max.) | 5mA | 1.6mA | 5mA |
| Maximum Angular Velocity | +/-300deg./sec. | +/-300deg./sec. | +/-300deg./sec. |
| Output (at Angular Velocity=0) | 1.35Vdc | 1.35Vdc | 1.35Vdc |
| Scale Factor | 0.67mV/deg./sec. | 0.67mV/deg./sec. | 0.67mV/deg./sec. |
| Resolution |  |  |  |
| Temp. Coefficient of Scale Factor | +/-20% at -5~+75°C | +/-20% at -5~+75°C | +/-20% at -5~+75°C |
| Linearity | +/-5%FS | +/-5%FS | +/-5%FS |
| Offset Drift (max.) |  |  |  |
| Response (max.) | 50Hz | 50Hz | 50Hz |
| Noise Level (max.) |  | 20mVp-p |  |
| Min. of Operating Temp. Range | -5°C | -5°C | -5°C |
| Max. of Operating Temp. Range | 75°C | 75°C | 75°C |
| Min. of Storage Temp. Range | -30°C | -30°C | -30°C |
| Max. of Storage Temp. Range | 85°C | 85°C | 85°C |
| Weight (g) (max.) | 0.4g | 0.2g | 1.0g |